SETTING  UP:

- Hook up suitable size tractor

Recommended:	 18T		150 – 220 HP

- Plug in remotes:

2 hoses for auger drive

2 hoses for auger ram

1 hose for case drain

# Test to make sure they operate the correct way

- Make sure tyres are inflated to correct pressure  -  225KP

- When operating the discharge auger only allow it to fold and unfold at slow speed or damage can occur.  Set flow control to slow.

- Floor Auger: - make provision for 12v connection and switch to be able to switch it off when necessary.  The floor auger may need to be turned off when field bin or truck is full and you need to travel some distance to fully empty chaser bin.  Also to empty main auger to be able to lower it to transport position for safe travel

SERVICE:

Grease: 	There are 4 bearings that need greasing every day.

1 grease point in the centre fold that needs greasing every 4 hours

OPERATION:

Before operating, do a position check while not travelling to determine a working position.   While working header driver should maintain two-way contact.

To operate with full hydraulic drive, you need to turn off the floor auger electrically, turn on the hydraulic drive to the augers with tractor controls to set speed of the discharge auger by adjusting tractor flow control.  To start operations, turn on the floor auger electrically.

To adjust floor auger for maximum output refer: Illustration (aa)

Every situation is different but for most places it is best to travel towards field bin while being filled from harvester, so that when you have a full bin you don’t have very far to go with a full load.  It is best when bin needs to be emptied that you pull up to field bin, put out unloading auger move into right position and start the main auger, then speed up tractor engine to an appropriate discharge speed.

CLEAN  OUT:

To completely clean out bin, open drop doors under bin to allow all grain to fall to ground.  Put back and use over centre catches to secure doors firmly.

SAFETY:

NEVER climb into bin while it is working.

Keep hands and feet away from moving parts.

Always replace guards if removed for maintenance.

Remember hydraulic hoses are under pressure while working so be careful when using hydraulics.

Turn off bin and tractor when carrying out work on bin.

If you ever come into contact with power lines, the safe way to dismount is to turn off machinery and jump well clear without touching machine and ground at the same time and contact authority to clear machine.

Travel at a safe speed appropriate to ground conditions so as to eliminate any bounce.  Excessive speed will cause damage to structure through metal fatigue.

MCDOUGALL  CHASER  BIN

Model: ..………………………………………………………………….

Serial No: ………………………………………………………………..

Date of Purchase: ………………………………………………………..

Description of goods: …………………………………………………….

……………………………………………………………………………

……………………………………………………………………………

……………………………………………………………………………

Illustration (aa)

Compensated Flow Control Valve:

The compensated flow control valve fitted to hydraulic chaser bin is supplied with oil from the tractor hydraulics via quick couplers or high flow outlet.

Oil flow from the compensated flow control is then directed to the floor auger hydraulic motor from the compensated flow control ‘P’ port and from the ‘B’ port to the discharge auger hydraulic motor.  Oil from the outlet port of the floor auger hydraulic motor combines with oil from the compensated flow control ‘B’ port to provide a continuous oil flow to the discharge auger hydraulic motor.

Discharge Auger Motor:

Auger speed is fixed by the volume of oil supplied by the tractor.  No  adjustment to hydraulic motor speed is provided by the compensated flow control.

Floor Auger Motor:

The floor auger hydraulic motor is adjustable for speed and torque (power) by separate controls provided on the compensated flow control.

Also manual/electric control over the floor auger motor is also provided as a means of turning the floor auger on or off as required by the operator.

Compensated Flow Control:

PORT ‘E’  -		Oil supply to valve from tractor

PORT ‘B’ -		Unregulated oil flow to inlet port of discharge auger motor

PORT ‘P’ -		Priority regulated port for oil supply to floor auger motor

PORT ‘T’ -		Drain Line – Return to oil tank

Relief Valve -	Set to control power (ie pressure) to floor auger motor

designed to stop floor auger motor from overloading 					discharge auger – Provides automatic power control over 					floor auger.  Turn adjusting screw clockwise to increase 					pressure setting.

Electric Solenoid - 	Manual / electric control of floor auger.  Apply 					electrical power to solenoid coil, will turn off floor auger.  				Turn off electrical power will “turn off” floor auger

Flow Control Adjustment:	Provides flow control or speed control to floor

auger.  Oil flow increases with clockwise rotation of

adjusting screw on version 2 valves and anti clockwise 					rotation on version 1 valves.

Version 1 and version 2 valves are identical in function and operation.

SPEEDS REQUIRED:				(Nominal tractor flow 90LPM)

Floor Auger Motor

Size: 		264cc/rev   @ 337 RPM    = 89 LPM

Adjustable 	-	0 - 	430 ( @ 115 LPM)

Discharge Auger Motor

Size:  		198cc/rev   @ 450 RPM    =    89 LPM

550 RPM    =  115 LPM

POWER

Maximum system pressure set by tractor

Floor Auger	-	Adjustable by relief valve on compensated flow 					control (50 – 210 Bar) turn adjusting screw clockwise to 					increase pressure (power) to floor auger motor.

Discharge Auger	-	Power set by tractor hydraulics

# Text boxes

Port ‘E’

E

P

B

SUPPLY OIL

COMPENSATED FLOW CONTROL

DISCHARGE AUGER

HYDRAULIC MOTOR

FLOOR AUGER

HYDRAULIC AUGER

RETURN OIL

SIMPLE CIRCUIT

Increase Flow

Port ‘T’

Flow Adjustment Screw

Dual coupling to provide

better oil supply for tractors

without high flow outlet

VERSION 2 VALVE

PORT

‘P

PORT

‘B’

12V DC

Electric Solenoid

12V DC

CHASER BIN HYDRAULIC CIRCUIT

Floor Auger Motor

Discharge Auger Motor

Pressure Control Adjustment

Flow Control Adjustment

Supply

Drain

Maximum flow in – 115LPM

B

P

E

Return

Compensated Flow Control

Check valve on ‘P’ port to provide better operation of compensated flow control.

Not adjustable

Relief Valve